## Slide 1
NEUROBYTES
HOME ANALYSIS WHY IT WORKS
EEG-TO-VIDEO RETRIEVAL
See what the brain
watched.
From three seconds of EEG over the visual cortex, NeuroBytes ranks 102 candidate videos and finds the one the person was watching. No video is shown to the model at test time, only brain activity.
36.03%
TOP-1 · CHANCE 0.98%
67.16%
TOP-5 · CHANCE 4.9%
5.99
MEAN RANK OF 102
×37
BETTER THAN CHANCE
Team NeuroBytes — Sushruth Shivaraju & Ayush Shetty
01
Notes: Hi, we're team NeuroBytes: Sushruth Shivaraju and Ayush Shetty. Our question was simple: can you tell which video someone watched, just from their brain activity? We take three seconds of EEG from 17 electrodes over the visual cortex and rank 102 candidate videos. The model never sees the video at test time, only the brain signal. Our final system, C13, puts the right video first 36% of the time and in the top five 67% of the time. Chance is under one percent, so that's about 37 times better than guessing.

## Slide 2
HOW IT WORKS
Three seconds, five steps.
01
Record
3 s of EEG while a clip plays
02
Window
0–700 ms after the clip starts
03
Decode
EEG → V-JEPA, CLIP, DINOv2, audio…
04
Fuse
rank fusion of ~650 scorers
05
Balance
CSLS hub removal + Sinkhorn
EEG Moments data
6 people, 17 channels over the back of the head, ~1,000 training clips each, 102 test clips.
~650 brain-to-video scorers
Ridge decoders over latency windows × deep video features, plus a contrastive net across people.
Cognitive grounding
The decodable signal sits in the first 800 ms — the classic visual ERP window.
Validated on held-out data
Every weight is chosen on held-out training videos; the test set only measures the result.
NEUROBYTES · EEG-TO-VIDEO RETRIEVAL
02
Notes: Here's how it works, in five steps. First, record: three seconds of EEG while a clip plays. Second, window: we only look at the first 700 milliseconds after the clip starts; more on why in a moment. Third, decode: we map the EEG onto features from deep video models like V-JEPA, CLIP and DINOv2, plus audio. Fourth, fuse: about 650 separate scorers each produce a ranking, and we combine them by rank, so they never need to be calibrated against each other. Fifth, balance: we remove "hub" videos that look like a match for everything, and use Sinkhorn so each video is picked roughly once. Every setting was chosen on held-out training videos. The test set was only used to measure the result.

## Slide 3
RESULTS
From 11% to 36% top-1
Official dev test, sub-01..04 (408 recordings, 102 candidates each).
FROM BASELINE TO FINAL SYSTEM
top-5
top-1
0%
20%
40%
60%
80%
30
11
J1
ridge baseline
36
12
T1
time-resolved
39
14
T2
V-JEPA 2 + S3D
52
23
WF1
winfuse 509
57
26
C3
both pipelines
62
31
C5
+ CSLS
67
33
C10
+ align, Sinkhorn
66
35
C11
+ neural net
67
35
C12
+ 7 heads
67
36
C13
+ 2 neural nets
NEUROBYTES · EEG-TO-VIDEO RETRIEVAL
03
Notes: This chart is the whole journey. Our first ridge baseline, J1, got 11% top-1. The winfuse pipeline, with 509 latency-window scorers, more than doubled that to 23%. Combining both pipelines took us to 26 and a half. Correcting for hubness pushed top-five past 62%. Cross-person alignment and Sinkhorn balancing reached 66.7% top-five. Finally, two contrastive neural networks trained across all six people gave C13: 36% top-one, 67% top-five. Every step stayed in only if it improved validation.

## Slide 4
THE FINDING
The signal is the onset response
Mean rank of the true video (of 102) when decoding from one latency window only. Lower is better; chance is 51.5.
0
20
40
60
chance 51.5
36
50–200
27
50–400
33
200–500
46
480–830
48
910–1260
52
1340–1690
51
1760–2110
51
2190–2540
50
2620–2970
window after clip onset (ms)
NEUROBYTES · EEG-TO-VIDEO RETRIEVAL
04
Notes: The most important finding is about timing. Here we decode from one time window at a time, and a lower bar means the right video ranks higher. The best window is 50 to 400 milliseconds after the clip starts. That is exactly where visual neuroscience places the P1 and N1 responses that encode objects and faces. After about 800 milliseconds, every window sits at chance, the line across the top. So most of a three-second recording says nothing about which video is on screen. Our biggest gain didn't come from a bigger model. It came from knowing when to look.

## Slide 5
WHY IT WORKS
What the brain signal can and cannot tell us
800 ms
The decodable signal is the onset response
Decoding is strongest 50–400 ms after the clip starts, the visual P1/N1 window. Every window after ~800 ms is at chance.
CSLS
Hubs and balance
CSLS removes each candidate's average pull; Sinkhorn makes every video win about once across the 102 recordings. Together ≈6 points of top-1.
6 brains
Learning across people needs alignment
The 17 channels mix brain sources differently in every head. A per-person spatial map lets each person borrow the others' recordings.
V-JEPA 2
Deep video models speak the brain's language
Self-supervised video models and mid-level CNN layers match the early visual response best. Interpretable attributes add nothing on top.
robust
Robust, not random
Same seeds rebuild bit-identically; five new seeds give 34.31 / 67.65 vs 36.03 / 67.16 — within one standard error (≈2.4 pts).
r = 0.16
Misses are noise, not hard videos
Per-video difficulty barely correlates between people. The true video is usually rank 2–5; single-recording noise decides the last step.
NEUROBYTES · EEG-TO-VIDEO RETRIEVAL
05
Notes: So why does it work? Four lessons. One: the decodable signal is the onset response. Two: the structure of the task matters. Removing hubs and balancing with Sinkhorn added about six points of top-one without touching the EEG at all. Three: you can learn from other people's brains, but only after aligning them. Every head mixes the signals differently, and pooling without alignment actually hurts. Four: it's robust. Rebuilding from scratch is bit-identical, and new random seeds stay within one standard error. The misses are mostly noise, not hard videos; the right answer is usually in the top five. With more repeats per clip and larger pretrained EEG models, we think this can go further. Thank you.